## Slide 1: EEG Based Brain Source Localization for Healthcare Applications CPD (0.5 point)
Engr. Dr. Munsif Ali H. Jatoi
Associate Professor,
Faculty of Engineering, Science and Technology,
Indus University, Karachi

## Slide 2: Presentation Outline
Presentation Outline
Introduction
Brain: Lets explore it
Why Brain Source Localization: A detailed introduction
Healthcare Applications
Research Outcomes
Conclusion

## Slide 3: Brain: Lets explore it…
The Human brain is most complex organ with 1012 neurons which are interconnected via axons and dendrites and 1015 synaptic connections.
This complex structure allows it to release/absorb quintillion of neuro-transmitter and neuro-modulator molecules per second.
The metabolism phenomenon of the brain can be analyzed through radioactively labeled organic molecules or probes that are involved in the processes of interest such as glucose metabolism or dopamine synthesis.

## Slide 4: Brain: Lets explore it…
The brain development starts at a primary age of 17-18 week of parental development and generates the electrical signals till death.
Neurons are acting as processing units for the brain activity to send or receive signals from/to various parts of body to brain.
According to embryonic developments, human brain can be divided into three regions anatomically which are: the forebrain (or prosencephalon), midbrain (or mesencephalon) and the hindbrain (or rhombencephalon).

## Slide 5: Brain: Lets explore it…
Brain tissues are categorized as either gray matter or white matter.
The brain regions formed by gray matter are of processing and connections. This matter is formed from unmyelinated neurons
mostly.
The white matter is composed of myelinated neurons which are used as connecters to gray matter.
White matter performs as to increase the speed between the connections.

## Slide 6: Brain: Lets explore it…
The brain cells are either neurons or neuroglia. Neurons are acting as processing unit for brain for sending/receiving information from/to various parts of the body to brain.
It contains a cell body which is called as soma, a nucleus, a dendrite tree and an axon.

## Slide 7: Brain: Lets explore it…
The brain surface is divided into four lobes which are: frontal lobe, parietal lobe, temporal lobe and occipital lobe respectively.
Each of lobe has specified functionality associated with it.

## Slide 8: Brain: Lets explore it…
The functionalities of brain lobes are defined as under:
Frontal lobe
-Behaviour, emotions, parts of speech, reasoning, creative thinking.
-Judgment, reasoning, problem solving.
-Speaking and writing
-Movement
-Intellectual thinking, attentiveness, self-awareness.

## Slide 9: Brain: Lets explore it…
Parietal lobe
Parietal lobe
-Sensory intelligence (sense of touch, pain, temperature etc.)
-Interpretation of signals from visual, audio stimuli.
-Spatial and visual perception.
Temporal lobe
-Language perception
-Memory
-Listening
-Sequencing and organization.
Occipital lobe
-Visual processing (light, color, movement).

## Slide 10: Brain: Lets explore it…
The electrical signals which are measured by neuroimaging techniques such as EEG, MEG, fMRI and PET are produced due to bioelectromagnetism inside the brain.
This electromagnetic activity is due to any physical or mental task.
This procedure is dependent upon the rise/fall of electrical potentials at the cell membrane.
The signals in the dendrites are termed as post-synaptic potentials (PSPs) and the signals emitted, moving along the axon are said to be action potentials (AP).

## Slide 11: Why Brain Source Localization?
The field of functional brain imaging is multidisciplinary research field that includes techniques dedicated to a better understanding of the human brain.
They does it through noninvasive imaging electrophysiological, hemodynamic, metabolic, and neurochemical processes that are going in normal and pathological brain.
One aim of using such neuroimaging techniques i.e. M/EEG is reconstruction of brain activity through non-invasive measurements of the associated bioelectromagnetic fields.

## Slide 12: Why Brain Source Localization?
This field of brain source localization or reconstruction using M/EEG signals is emerged few decades ago in neuroscience.
This brain source localization has variety of clinical and research applications.
The solution towards this localization problem involves the simulation of field distribution on head surface for a given current sources in brain and consequently localization of current dipoles by using various optimization algorithms.

## Slide 13: Why Brain Source Localization?
The brain source localization is done by using various neuroimaging techniques.
These techniques include MEG, EEG, fMRI and PET which have different temporal and spatial resolutions.
However, when the estimation of the location and distribution of the current sources due to which electromagnetic activity produced in the brain is measured through voltages, then its termed as EEG source localization.

## Slide 14: Why Brain Source Localization?
The problem is termed as source localization or EEG inverse problem because the data (potentials) is given and the model is constructed from data.
Mathematically, this problem is ill-posed as number of unknown parameters i.e. active brain sources is being greater than number of known parameters which is limited number of electrodes placed on scalp.
There is no unique solution to inverse problems in general and EEG inverse problem in particular.
Hence, the problem needs to be solved through stable way with minimization of error imposed.

## Slide 15: Why Brain Source Localization?
The methods used to solve inverse problem are listed below:
Deterministic Inverse problems: In such methods, regularization is needed as they have worst case convergence with infinite dimensional space. However, there is no assumption of noise to be made on measurements.
Statistics: In these types of ill-posed problems, estimators are applied for the solution. The dimension is finite with noise assumed to be randomly distributed for the measurements.

## Slide 16: Why Brain Source Localization?
Bayesian Inverse problems: For these inverse problems, posteriori distribution is maximized through any optimization algorithm to get unknown parameters. The dimension is assumed to be finite. However, the prior and noise are assumed with any distribution with most of the cases as Gaussian.
Control Theory: These inverse problems deal with infinite dimensional space. Thus, there is no assumption taken for noise for the system measurements.

## Slide 17: Why Brain Source Localization?
Generally, there are two approaches to solve inverse problem for EEG signals.
These are categorized as either parametric or imaging methods.
For the parametric methods, it is assumed that sources are represented by a few equivalent current dipoles of unknown locations and moments. These dipoles are then supposed to be estimated through non-linear numerical method.
On the other hand, the imaging methods are based on the assumption that primary sources are intracellular currents in the dendritic trunks of the cortical pyramidal neurons, which are aligned normally to the cortical surface.

## Slide 18: Why Brain Source Localization?
The solution for EEG brain source localization has two major steps:
- Solution of forward problem which involves the head modelling by using various numerical techniques.
- The mathematics related to this is defined in later slides.
- Solution of inverse problem by using various optimization algorithms.

## Slide 19: Why Brain Source Localization?
The forward modelling is done by using various numerical techniques such as finite element method (FEM), boundary element method (BEM), finite difference method (FDM) and finite volume method (FVM) respectively.
FEM uses volume for computational points while BEM uses surfaces for modelling.
BEM has direct inversion while FEM and FDM have iterative procedures.
BEM is less computationally complex and thus frequently used.

## Slide 20: Why Brain Source Localization?
For the explanation of forward modelling, it is necessary to learn about bioelectromagnetic phenomenon going inside the brain.
The electromagnetic activity is governed by Maxwell’s equations which define the relationship between electric and magnetic quantities.
These equations are defined in both differential and integral form to explain the quantities for quasi-static approximation of brain waves as we shall see later on.

## Slide 21: Why Brain Source Localization?
The Maxwell’s equations in differential and integral form are written below:
Differential form:

## Slide 22: Why Brain Source Localization?
Integral form:

## Slide 23: Why Brain Source Localization?
The brain signals generated have low frequency region which is less than 100 Hz.
For this, so called quasi-static approximation is taken into consideration.
This approximation says that the time derivative component in the Maxwell’s equations is ignored.
According to the literature, the tissue conductivity for head region at the frequency of 100 Hz is 0.3 with relative permittivity

## Slide 24: Why Brain Source Localization?
The EEG source localization is formulated through the given model:
where is EEG data matrix, L is the Leadfield or gain matrix, is current density matrix, is the error matrix due to artifacts.
As number of dipoles, Nd, is greater than number of sensors Nc, the problem becomes ill-posed one and regularization term is required in the solution.

## Slide 25: Why Brain Source Localization?
Coming back to discussion for inverse problem, it is ill-posed problem which is solved through optimization algorithms.
These optimization algorithms are categorized according to the formulation they look for.
The techniques are developed on least square (LS) formulation, subspace factorization, Genetic Algorithm (GA) and Bayesian modeling.
These techniques are classified according to their performance based on localization error and free energy as we shall see later on.

## Slide 26: Why Brain Source Localization?
Different methods were proposed for the solution of inverse problem using EEG:
  Class of low resolution techniques:
    LORETA, sLORETA, eLORETA, and their hybrids WMN-LORETA, SSLOFO etc.).
  Class of high resolution subspace based techniques:
    (MUSIC, ROOT MUSIC, Min. Norm, ESPRIT etc.)
  Class of Bayesian model based algorithms:
    (Multiple Source Priors (MSP))

## Slide 27: Why Brain Source Localization?
Minimum Norm Estimation (MNE)
  Developed by Matti S. Hamalainen in 1984.
  It works upon the principle of minimization of norm such that the solution is given by:

## Slide 28: Why Brain Source Localization?
Low Resolution Brain Electromagnetic Tomography (LORETA)
  Developed by R.D.Pasqual-Marqui in 1994.
  LORETA produces discrete, 3D distributed, linear inverse solution with improved time resolution but low spatial resolution.

## Slide 29: Why Brain Source Localization?
Bayesian Framework based Multiple Sparse Priors (MSP)
  Developed by Karl Friston and Jose’ David Lopez in 2014.
  Works upon the principle of Bayesian approaches.
  The noise is assumed to be Gaussian.
Hence, the estimated value of current density is given by:

## Slide 30: Healthcare applications
The brain source localization is multidisciplinary field as we saw previously.
It combines applied mathematics, signal/imaging and neuroscience analysis.
Hence, the effort to understand the brain source localization problem was started approximately 40-years ago by correlating the existing brain’s electrophysiological information to the basic physical principles controlling the volume currents in conductive media as mentioned in previous sections.
The information acquired through the brain source localization based on EEG signals is helpful to diagnose different brain disorders such as epilepsy, schizophrenia, depression, Alzheimer, Parkinson etc.

## Slide 31: Healthcare applications
Among them, the most common is epilepsy as according to world health organization (WHO) statistics, around 50 million of world population is diagnosed as epileptic.
This figure mounts to 40-70 % per 0.1 million peoples in developing countries which is quite alarming situation.
Furthermore, more than 80% cases are reported in developing countries with ¾ of them not receiving proper treatment which includes the diagnoses through neuroimaging techniques and providing of anti epileptic drugs (AEDs).

## Slide 32: Healthcare applications
Economically, epilepsy accounts for 0.5 % of the global burden on economy and growth which is very huge amount as compared to other brain disorders.
In some underdeveloped countries such as India, the cost per case was reported as 344 USD.
However, the social effects on the life of epileptic person are varied from country to country. It includes the restriction to marry, to go for restaurants, theatres and clubs and other public buildings etc.

## Slide 33: Healthcare applications
Epilepsy can be treated by providing anti-epileptic drugs (AEDs) or by surgical therapy prior to which diagnoses is carried out by using neuroimaging techniques.
Hence, brain source localization techniques are used to localize epileptogenic regions where the abnormal behavior of neurons can be observed during a seizure.
Also, the localization information can help clinicians to operate brain tumor as it is one of reasons behind secondary (or symptomatic) epilepsy.

## Slide 34: Healthcare applications
Another important brain disorder is schizophrenia which has affected more than 21-million peoples around the globe.
It is characterized by disruptions in thinking, affecting language, perception and losing the sense of self.
This disorder grows in late adolescence or in early adulthood. The major drawback of this chronic disorder includes the drowsiness, dizziness with changing positions, blurred vision, rapid heartbeat, skin rashes and so forth.

## Slide 35: Healthcare applications
Brain source localization methods such as LORETA and sLORETA are applied to determine the region of abnormality for schizophrenic patients.
These power maps were compared to show difference between schizophrenic and control subjects.
In another study, a low resolution source localization technique, eLORETA was used to define functional connectivity and source localization for schizophrenic subjects.
Also, BSS techniques are used for localization of P300 sources in schizophrenia patients.

## Slide 36: Healthcare applications
Depression is also one of the common brain disorders characterized by sadness, loss of interest or pleasure, guilt feeling, disturbed sleep or appetite etc.
It can be categorized as either mild or severe. In the severe case, most cases are reported with suicidal attempts.
It is reported in research works that brain source localization techniques (such as LORETA) are applied to localize the position of region most affected by major depression disorder (MDD).

## Slide 37: Some Research outcomes
tcomes
Generated source activity at SNR=5dB

## Slide 38: Some Research outcomes
MSP results
LORETA results
MNE results
OP-MSP results

## Slide 39: Conclusion
This CPD discussed the EEG based brain source localization and its healthcare applications.
It was observed that brain source localization is multidisciplinary field with its roots in neuroscience and applications from brain disorders.
The proper healthcare applications were discussed for various brain disorders which include epilepsy, schizophrenia, depression and stress.
Some of the results for brain source localization using various techniques were produced for synthetically generated EEG data.

## Slide 40: Conclusion
Future plan is launching of BrSA (Brain Sciences Awareness) program nationwide to impart awareness for various brain disorders.