## Slide 1: Keynote Talk Introduction to Statistical Signal Processing
Engr. Dr. Munsif Ali H. Jatoi
Associate Professor
Salim Habib University

## Slide 2: Presentation Outline
Introduction
Statistics behind SSP
Applications
Conclusion

## Slide 3: Introduction
Majority of signals within nature as well as synthetic are having stochastic structure.
The noise is imparted/induced in the original signal thereby distorting the quality of signal.
For example: Channel noise disturbing communication system…

## Slide 4
The signals having stochastic nature are modelled with the help of probabilistic modeling.
The compression theory uses probabilistic models for every compressed signals.
Measurement of physical phenomena such as earthquake, brain signals, heartbeat etc. are stochastic in nature.
Introduction

## Slide 5: Introduction
Thus, it is necessary to extract the signal or parameter of interest from degraded measurements due to noise.
This can be achieved through the application of statistical models; diverse sensors which acquire extra spatial, temporal or polarization information or multidimensional signal representation i.e. time-frequency etc.
This gives rise to develop signal estimation, detection and tracking algorithms.

## Slide 6: Introduction
The statistical signal processing works on the assumption of random signal and provides estimation, detection and tracking using statistical tools.
Owing to the fact that random signals are unpredictable in time domain, yet their average statistical properties exhibit considerable regularity.

## Slide 7: Introduction
Hence, dealing with random signals, the main objectives for SSP to achieve are statistical description, modelling and exploring the dependence of for various parameters.
The SSP has got multiple processes in it with various applications in diversified fields.

## Slide 8: Some random signals
Speech Signal
Seismic Signal

## Slide 9: Some random signals
EEG Signal
ECG Signal

## Slide 10: Some random signals
Radar Signal
SONAR Signal

## Slide 11: Processes
SSP typically involves various modules such as:
      Signal modelling by random processes
      Estimation of the model parameters
      Signal Estimation by Optimal Linear Filters
      Power Spectrum Estimation
      Signal Detection

## Slide 12: Processes

## Slide 13: SSP basic concepts
To understand various concepts behind SSP, we need to revise some basic definitions related to SSP theory.
Random Variable (Stochastic Variable):
    A random variable x is a single valued, real or complex function defined on sample space of some event assigning a real number to each sample point of sample space.
    Random value is characterized by probability distribution.

## Slide 14: SSP basic concepts
Probability
Random variable X
Sample Space

## Slide 15: SSP basic concepts
Distribution Function:
    A distribution function (or cumulative distribution function (CDF)) of a random variable X is the function defined as:
    This function is non-decreasing function with range defined as:

## Slide 16: SSP basic concepts
Discrete Random Variable:
    A random variable X which is defined on discrete levels or its CDF changes values only in discrete instances than it is termed as discrete random variable.
    The probability mass function is defined for discrete random variable.

## Slide 17: SSP basic concepts
Continuous Random Variable:
    A random variable X which is defined on continuum levels and also has a derivative dFx(x)/dx which exists everywhere at some points then the rv is termed as Continuous rv.
    The probability density function (pdf) is defined for continuous random variable such that:

## Slide 18: SSP basic concepts
Some Important PDFs
(Discrete and Continuous):

## Slide 19: SSP basic concepts
Expected Value (MEAN) of Random Variable:
    The expected value or mean for a RV is defined as:
    The mean is of rv is center of mass of probability density/mass function. It obeys linearity i.e. E(aX)=aE(X).

## Slide 20: SSP basic concepts
Moment of Random Variable:
    The nth moment of a rv X is defined by:
    The mean of a rv is the first moment of X.

## Slide 21: SSP basic concepts
Variance of Random Variable:
    The variance for a RV denoted by σ2 or Var(X) is defined as:
Thus,
It should be noted that:

## Slide 22: SSP basic concepts
Standard Deviation of Random Variable:
    The standard deviation of a rv X, denoted by σx, is the positive square root of Var(X).
    Thus,

## Slide 23: SSP basic concepts
Moment of Random Variable:
    The normalized third centralized moment is skewness which is defined as:
    The skewness of rv is the third moment of X which is asymmetry of the data around the sample mean.

## Slide 24: SSP basic concepts
Moment of Random Variable:
    The normalized third centralized moment is kurtosis which is defined as:
    The kurtosis of rv is the fourth moment of X and is termed as outlier-prone in the data.

## Slide 25: SSP basic concepts
Covariance and Correlation Coefficient:
    The (k,n)th moment of a bivariate rv (X,Y) is defined by:
If n=0, the kth moment of X is obtained and if k=0,
the nth moment of Y is obtained.

## Slide 26: SSP basic concepts
Covariance and Correlation Coefficient:
    Hence by assuming m11, variances of X and Y are calculated as:
    The covariance of X and Y, denoted by Cov(X,Y) or σXY, is defined by:
    If Cov(X,Y)=0, then X and Y are uncorrelated.

## Slide 27: SSP basic concepts
Covariance and Correlation Coefficient:
    The correlation coefficient, denoted by ρ(X,Y) or ρXY, is defined by:
    It should be noted that:
    The correlation coefficient shows the linear dependence between X and Y.

## Slide 28: SSP basic concepts
Correlation Matrix:
    For an n tuple of random variables, X=[X1,X2,…,Xk]T, there are k2 pairs of random variables and associated correlations:
    This is the matrix of pairwise correlations:

## Slide 29: SSP basic concepts
Covariance Matrix:
    For an n tuple of random variables, X=[X1,X2,…,Xk]T, the matrix of covariances with (i,j)th element:
    In the matrix formation:

## Slide 30: SSP basic concepts
Stochastic processes:
    A stochastic or random process is the assignment of a function of a real variable to each sample point ω in the sample space.
    Thus, the process X(ω,t) can be considered as a function of two variables.
    Each time function of the process is called a sample function and must be defined over the entire domain of interest.

## Slide 31: SSP basic concepts
Estimation Theory:
    Let X be a rv with pdf f(x;ϕ) which dependes on an unknown parameter ϕ.
    Let X1,X2,…,Xn be a random sample of X. Thus, an estimator of ϕ is any statistic s(X1,X2,…,Xn) denoted by:
The value of estimator will be called an estimate of ϕ.

## Slide 32: SSP basic concepts
Example: Brain Source Estimation using Bayesian Estimation
    The Generalized linear model (GLM) for EEG measurements is provided as:
    Here, are EEG recordings,
    is the current density needs to be estimated using estimation techniques, ε is Gaussian noise.

## Slide 33: SSP basic concepts
Example: Brain Source Estimation using Bayesian Estimation
    This inverse problem can be solved through various statistical signal processing methods such as minimum norm estimation, second order Laplacian, multiple signal classification (MUSIC) and Bayesian based Multiple sparse priors (MSP) technique.
    The results are characterized by localization error and free energy.

## Slide 34: SSP basic concepts
Example: Brain Source Estimation using Bayesian Estimation
    Some of the results after applying these methods on real time EEG data are shown below:

## Slide 35: SSP basic concepts
Example: Brain Source Estimation using Bayesian Estimation

## Slide 36: SSP basic concepts
Example: Brain Source Estimation using Bayesian Estimation

## Slide 37: SSP basic concepts
Example: Brain Source Estimation using Bayesian Estimation